## Slide 1
// AERO HACKATHON · SHOW & TELL
From sensor to cockpit over a real ARINC 429 bus
A Sensor Unit and a Secondary Flight Display, built the way certification-grade avionics are built.
Humans X AI
SENSOR UNIT
═══ ARINC 429 ═══▶
SFD UNIT
Notes: [0:00–0:15] Hi. In five minutes: what we built, how we planned it, how it is designed, a live demo, and why it goes beyond the brief. One sentence: a sensor unit reads the outside world and publishes it on a real ARINC 429 bus; a Secondary Flight Display unit receives it and shows it to the crew.

## Slide 2
// THE CHALLENGE
Three layers asked. Two avionics units delivered.
The brief
01
Embedded: firmware on real or simulated hardware, acquiring sensor data.
02
Backend: flight-data logic and communication between components.
03
Frontend: a cockpit-style display presenting live flight data.
Our answer
SENSOR UNIT
Reads the world, speaks A429
A USB gamepad mimics the external quantities. Bare-metal Cortex-M3 firmware in QEMU acquires them and transmits 6 ARINC 429 labels at 50 Hz.
SFD UNIT
Receives, validates, displays
Backend decodes and judges validity; frontend renders the Secondary Flight Display and its configuration page.
Joined only by the A429 bus
Notes: [0:15–0:40] The brief asks for three layers: embedded, backend, frontend. We mapped them onto how real aircraft are integrated: two units, two LRUs. The Sensor Unit - gamepad as the outside world, ARM firmware as the sensor computer - and the SFD Unit - backend plus frontend as one display device. The only thing they share is an ARINC 429 bus. That choice drives everything else.

## Slide 3
// THE PLAN
Interfaces first. Every decision on record.
Before a single line of code, every requirement was answered explicitly and written into PLAN.md: no guessing, no silent assumptions.
01
11 requirements agreed up front
02
6 A429 labels: pitch, roll, heading, baro altitude, CAS, vertical speed
03
Wire contracts fixed first: A429 word, label table, pad frame
04
Capture-first: backend and SFD built on a recorded bus, never waiting on QEMU
Milestones — each closed by a proof command
M0
Toolchain ARM GCC + QEMU verified
M1
A429 codec golden vectors
M2
Firmware boots in QEMU
M3
Pad reader live axes over TCP
M4
Backend decode, convert, freshness
M5
Displays SFD + config page
M6
End to end + decoupled replay
Notes: [0:40–1:15] We spent the first minutes deciding, not coding. Eleven requirements, each from an explicit answer, are on record in PLAN.md. We fixed the interfaces first - the A429 word, the shared label table, the pad frame - because that is the cheapest place to be wrong. And we went capture-first: we recorded the bus once, so the backend and display never waited for the emulator. Seven milestones, M0 to M6, each closed by a command that proves it - not by "it works on my machine".

## Slide 4
// ARCHITECTURE · SDD
Two units. One bus. Nothing else shared.
SENSOR UNIT
SFD UNIT
Gamepad
external
environment
USB
Pad reader
host acquisition
UART
Firmware
Cortex-M3 · QEMU
flight model
ARINC 429
6 labels · 50 Hz
Backend
decode · convert
validity
SSE
Frontend
SFD + config
page
Replaceable: real sensor, other simulator or a recording
Never knows the source
01
Firmware writes UART registers — it does not know QEMU is there: porting to hardware is a wiring change.
02
The A429 bus is the seam — the SFD Unit runs unchanged with the Sensor Unit swapped for a recording.
Notes: [1:15–2:00] This is the design document in one picture. Left, the Sensor Unit: the gamepad stands in for the outside world, a host reader acquires it, and bare-metal ARM firmware runs the flight model at 50 Hz and encodes six ARINC 429 labels. Right, the SFD Unit: the backend decodes, converts to engineering units and judges validity; the frontend renders the display. The red line - the A429 bus - is the only thing they share. The firmware writes hardware registers and has no idea it runs in QEMU; the display has no idea where the words come from. The full rationale, ten-plus design decisions and the interface control document are in the documents folder.

## Slide 5
// DESIGN DECISIONS
Built to be trusted, not just to fly.
01
Decoupling is tested
Replay mode runs the whole SFD Unit with no QEMU, no gamepad and no bus port open. A test proves it.
02
One source of truth
Only the firmware produces values. Sliders configure the display window; they can never fake a value.
03
Validity end to end
Parity and label checks, NCD on FREEZE, and a 250 ms freshness watchdog that annunciates A429 LOSS.
04
Certification-minded
Backend only decodes, converts and validates. SDD and a DO-178C-structured ICD with traceable requirements.
Notes: [2:00–2:35] Four decisions make this trustworthy rather than just a demo. One: decoupling is not a claim, it is a test - the display path runs from a recording with the sensor unit absent. Two: one source of truth - nothing downstream of the firmware computes or overrides a value; the sliders change how it is shown, never what it is. Three: validity end to end - corrupted words are rejected, FREEZE sends No-Computed-Data, and if the bus goes silent for 250 ms the SFD says so. Four: the backend stays deliberately simple and certifiable, and the interface is captured in a DO-178C-structured ICD.

## Slide 6
// LIVE DEMO
Fly it. Freeze it. Unplug it. Replay it.
01
Fly: stick moves attitude, heading, altitude and airspeed — all computed in the firmware.
02
Slider: narrow the pitch window — the scale changes, the value does not.
03
START: every label goes No-Computed-Data — the SFD flags it.
04
Stop the pad: after 250 ms every parameter is STALE — A429 LOSS warning.
05
Replay: no QEMU, no gamepad — the SFD flies again from the recorded bus.
# full stack
npm start
# decoupled
npm run start:replay
# open
:8090/sfd
:8090/config
Notes: [2:35–3:55] (switch to the two browser windows, SFD and config side by side) 1. Fly: bank and pull - horizon, heading, altitude and airspeed move. Nothing here is computed in the browser. 2. Slider: narrow pitch to plus-minus 10 degrees - the ladder ends there, readout turns amber beyond it, the value itself is untouched. 3. Press START: every instrument shows NCD - that is the sign/status matrix travelling over the bus. 4. Stop the pad reader: a quarter second later everything goes STALE and the A429 LOSS warning sounds. 5. Stop everything, npm run start:replay: no emulator, no gamepad - and the SFD flies again. That is the decoupling, live.

## Slide 7
// THE HIVE
An automated pipeline for integrating changes.
Verification on every change
01
64 automated tests incl. boundary values for every label
02
21 checks pad frame → firmware → A429 → backend, in QEMU
03
41 checks every parameter driven into both limits, in QEMU
04
Golden A429 vectors + decoupled replay tests
AI-framework branch: integration
01
5 AI agents embedded, backend, frontend, integrator, reviewer — each owns its paths
02
Rules + skills checked against the code by a script
03
Run chain M0–M9 one command per milestone
04
CI on every push / PR framework, tests, firmware in QEMU on Linux; pre-commit hook
Humans X AI Humans took every decision, on record. AI agents build, check and review — inside the paths they own.
Notes: [3:55–4:35] For The Hive: every change is checked automatically. On sandbox: 64 tests including boundary values per label, plus two harnesses that boot the real firmware in QEMU and push it to every limit - 21 and 41 checks. On the AI-framework branch we went further: five AI agents, each owning only its part of the repo, rules and skills that a script checks against the code, a run chain for milestones M0 to M9, and CI on every push and pull request - including building and running the firmware in QEMU on Linux. Humans X AI, as the theme says: humans decided, AI built and verified.

## Slide 8
// EXTRA MILE
Nobody asked. We did it anyway.
01
Real ARM firmware
Bare-metal Cortex-M3 with its own vector table and linker script — not a script called "firmware".
02
Bit-exact ARINC 429
Bit-reversed labels, BNR, sign in the SSM, odd parity. Corrupt words rejected and counted.
03
Physical gamepad
The stretch goal, read over raw HID with a WinMM fallback.
04
Coherent flight model
Nose up climbs, bank turns: attitude, V/S and altitude always agree.
05
Aural alerts
A429 LOSS warning, BANK ANGLE and SINK RATE callouts.
06
Certification documents
SDD and a DO-178C-structured ICD with requirement-to-test trace.
Thank you — questions?
Notes: [4:35–5:00] For the Extra Mile: real ARM firmware, a bit-exact A429 bus, the physical gamepad stretch goal, a flight model where attitude and altitude always agree, aural alerts, and certification-style documents - a design document and a DO-178C-structured ICD. Thank you - happy to take questions.